Design Manual

Lewis Lee - z3415068
Andrew Chan -

Overview:

The elevator system uses a finite-state based approach and is a state machine.
The main states are: Closed, Opening, Opened and Closing
There is also an inclusion of some custom flags: Direction flag, Moving flag, Emergency flag.
These are all determined by bits in a status register:
Bits 1 and 2 determine the state: 0, 0 = Door Closed 1, 0 = Door Opening
    0, 1 = Door Closing 1, 1 = Door Opened
Bit 4 determines the direction: 0 = Down 1 = Up
Bit 5 determines if the elevator is moving: 0 = Not Moving 1 = Moving
Bit 7 determines if the elevator is in an emergency state: 0 = Not emergency state
        1 = Emergency state
External Interrupts 4 and 5 are used for the close and emergency button respectively.
Timer 0 is used as an overflow interrupt to time each state.
Timer 1 is used to generate a PWM signal that controls the speaker.
Timer 2 is used to generate a PWN signal that controls the motor.

Macro Functions:

There are 9 Macro functions used:
4 LCD functions:
-lcd_write_com
Writes a command to the LCD
-lcd_write_data
Writes data for the LCD to display
-lcd_wait_busy
Waits until the LCD is no longer busy
-lcd_init
Initialises the LCD
4 Floor related functions:
-load_floor_temp
Given a floor, returns that floors request value
-set_floor_request
Given a floor and value, sets the floors request to the value
-check_floors
Returns whether any floors have requests or not
-check_floors_direction
Returns if any floors are requested in the direction of the elevator
1 Delay function:
-delay
Causes a small delay given a 2 byte number (delay = 1.08us * number)

Modules:

There are 10 Modules/Distinct routines:
-reset
Initialises the elevator by setting variables, pointers, interrupts, timers and the LCD
-Timer0
The timer0 overflow service routine; Counts required time and takes action according to	the various states.
-main
Constantly scans the keypad while the timer runs in the background
convert:
A function in main which takes in a keypad press and takes action according to its value.
-changeFloor
Changes the floor (under certain conditions) and controls the direction.
-openDoor
Opens the door (under certain conditions).
-closeDoor
Closes the door.
-holdDoor
Holds the door open.
-closeButton
Closes the door (under certain conditions) if the external interrupt is activated
-openButton
Opens the door or holds the door open (under certain conditions).
-emergency
Sets emergency conditions and carries out the emergency procedure
flash:
A function that is only active in emergency mode. Flashes the LEDs and speaker.

Data Structures:

Floor requests uses a 10 byte array in the data segment to store floor requests.
A value of 0 indicates the floor is not requested, any other value indicates the floor is requested.

The strings “Emergency” and “Call 000” are stored in the program memory.

All other variables are stored in an 8-bit register:
-temp = r16 Stores A temporary register
-temp2 = r17 Stores A temporary value
-count = r18 Stores a counter
-count2 = r19 Stores a counter
-floor = r20 Stores the current floor
-status = r21 Stores the status of the elevator
-row =r22 Stores the row for the keypad
-col =r23 Stores the column for the keypad
-mask =r24 Stores the mask for the keypad
-emergencyFlash = r25 Stores the LED value to display at emergency

System Control Flow:

Algorithm for Servicing Requests:

Floor requests are serviced by constant checking and moving through states.
The following sequence describes the logic of how a typical request is serviced.

///////////////////////////////
TIMER0:
Count one second:
If state = CLOSING call change floor, If state = OPENING call hold door.
Reset timer.
Count another second:
If state = CLOSED call open door.
Reset timer.
Count another second:
If state = OPENED call close door
Reset Timer.
///////////////////////////////
MAIN:
Scan keypad constantly
If key pressed call convert

CONVERT:
If a number, add a floor request to the corresponding number.
If a star symbol, call open door if CLOSING, or stop timer until button released if OPENING.
Return
///////////////////////////////
CHANGE FLOOR:
State = CLOSED
If no requests exist, remain on floor by recursing change floor, otherwise continue.
If request exists on current level, call open door. (For re-pressing a level, or if change floor was	recursing and current floor was pressed).
If no requests exist in current direction, change direction, otherwise continue.
Increment or decrement current floor according to direction.
Return

OPEN DOOR:
Check if current floor is requested
If requested: clear current floor request, open door (State = OPENING)
If not requested: call change floor.
Return

HOLD DOOR:
State = OPENED
Return

CLOSE DOOR:
State = CLOSING
Return
/////////////////////////////////